## Slide 1: Arduino IDE
Download and install instructions – https://arduino.cc
Single one-stop, editor, compiler and library for Arduino Systems
Board
  UNO board, UNO-clones using CH340 USB-serial interfaces
  Processors ATMega 328 (DIP, Quad-pack SMD)
  Experiment, test using UNO, prototype using Nano
  Require USB on laptop, USB cable for interfacing/power
Language for programming (Reference)
  Based on Processing
  Quite similar to C++

## Slide 2: Language Nuances (percularities)
Case-sensitive, each statement terminated with a “;”
Good programming practices
  One statement on one line
  Use tabulation/indentation to show nesting
  Full CAPS for constants, use const instead of #define
  Start all Class/objects with Capital letter
  All other variables start with lower case (camelCase recommended)
  Use /*..*/ and // for comments
Define all functions before setup() and loop()

## Slide 3: setup() - required
A function, which is run only once
Put all initialization and configuration statements here
  Configure for Input/Output
  Serial speed
  Initialization of global variables
  Setup of devices

## Slide 4: loop() - required
Also a function
Runs without stopping
When function ends, it restarts at the beginning
All variable declared within the function are local

## Slide 5: Processing statements
Copious library of functions
Also plenty of 3rd party libraries (sometimes too many)
Condition statement
  If-then-else
  switch – case
Loops
  for used for definitive number of loops (e.g. n times)
  while used for in-determinate number of loops (0, 1, or n times)
  do..while used for in-determinate number of loops, at least once (1,..n times)

## Slide 6: Digital Input/Output
Digital – values are only LOW (0V), or HIGH (5V)
Initialise/configure our Pins (0..13)
  pinMode ( <pinNumber>, <MODE> )
    INPUT - digital input pin (reads LOW, HIGH)
    OUTPUT – digital output pin (outputs LOW, HIGH)
    INPUT_PULLUP – same as INPUT but connects an internal 20K resistor
Input / Output
  digitalRead( <pinNumber> )
    Returns an integer based on the port reading value (LOW, HIGH)
  digitalWrite(<pinNumber>, <LOW|HIGH>)
    Outputs a LOW or HIGH to the pin

## Slide 7: Analog Input
Analog = variable voltage levels
Inputs using only A0..A5
Returns a value from 0..1023 based on
  Vref
  Voltage applied at the analog pin
Example, if 3.1V is applied at A1
  Value = analogRead(A1)
    Value returned = 3.1 * 1024/5 = nnn

## Slide 8: Analog Output
NO direct analog output
ATMega328 uses Pulse-Width Modulation (PWM)
Voltage is proportional to the duty-cycle
analogWrite(<pwm pin>)

## Slide 9: Serial IO Library
A neat way of troubleshooting your Arduino code.
Uses the Uno’s Tx and Rx pin to send data back to the IDE using the USB interface
Serial Library
  Serial.begin(<speed>) sets up comms speed (9600)
  Serial.print(), Serial.println() sends data back to the host
Use the Serial Monitor to check your answers